## Slide 1: ROACH2 RCU
Rover Control Unit - Systemdesign

## Slide 2: Structure
System requirements
System design
Components

## Slide 3: System requirements

## Slide 4: Tasks
The following tasks are mandatory for the RCU:
Control HV generator(s) and engines => control of the rover movement
Measure distances to surroundings => check if to reverse movement direction
Measure acceleration
Measure temperature
Measure supply voltages of:
  Engines
  HV generator(s)
  Processor system
  Sensors
  Memory/SD card reader (if implemented)
Communicate with OBC (Ethernet or USB/UART)

## Slide 5: Tasks
3D localization using multiple ToF sensors
Camera (VGA with 30fps or CSI interface)
Onboard data storage (SD card or NAND flash)
  Optional with error codes (CRC, FEC, …)

## Slide 6: System design
Sensors, actors and interface to OBC

## Slide 7: System design

## Slide 8: System design: Sensors

## Slide 9: System design: Actors

## Slide 10: System design
Firmware:
Main applications
  Experiment control
  Data acquisition system
  Test subsystem (not running in final experiment)
Driver
  I2C
  WLAN
  USB-Ethernet
  GPIO
  USB-UART
  SD card
  DVP camera

## Slide 11: System design
Requirements from proposal (aiming RCU directly):
Validation of the rover control unit (RCU) to track the movement and current rover status
  Components used therefore:
    Laser distance sensors (ToF distance sensor arrays)
    IMU
    Rotation encoder
  Task: 3D position localization
Capturing and saving pictures with a rover mounted camera
  Components used therefore:
    DVP camera (5MP)
    LEDs for illumination
  Tasks: Camera image stream acquisition

## Slide 12: Components
Sensors, actors and interface to OBC

## Slide 13: Sensors
Sensor | Task | Desired part | Units
IMU | Acceleration, orientation | Bosch Sensortec BNO055 | 1
Distance measurement sensor | Measure distance | ST VL5310X | 15+
Temperature sensor | Measure temperature | LM75AIMM | 1
Rotation encoder | Count rotations | ENX10 EASY 128IMP (?) | 1
ADC | AD conversion | MCP3426/7/8 | 1
Prices taken from Digikey and rounded up!

## Slide 14: Actors
Actor | Task | Desired part | Units
Motor driver | Motor driver | TI DRV8871DDAR | 1
HV generator | ? | ? | 1

## Slide 15: Thank you for attention!
Please feel free to ask questions?