## Slide 1: ROACH2
Rover Control Unit (RCU) Version 2

## Slide 2: Structure
System requirements
  Tasks
  Future upgrades
Components
  Sensors
  Actors
  Interface to OBC
Processor options
  Xilinx XUP
System design

## Slide 3: System requirements
System tasks and future upgrades

## Slide 4: Tasks
The following tasks are mandatory for the RCU:
Control HV generator(s) and engines => control of the rover movement
Measure distances to surroundings => check if to reverse movement direction
Measure acceleration
Measure temperature
Measure supply voltages of:
  Engines
  HV generator(s)
  Processor system
  Sensors
  Memory/SD card reader (if implemented)
Communicate with OBC (Ethernet or USB/UART)

## Slide 5: Future upgrades
The following list will only be implemented if the basic functions are implemented and operational:
3D localization (either on OBC only or on both, so that the RCU can validate the sensor return data more precise)
Camera (VGA with 30fps or CSI interface)
Onboard data storage (SD card or NAND flash)
  Optional with error codes (CRC, FEC, …)

## Slide 6: Components
Sensors, actors and interface to OBC

## Slide 7: Sensors
Sensor | Task | Desired part | Units | Price per unit | Total
IMU | Acceleration, orientation | Bosch Sensortec BNO055 | 1 | 11€ | 11€
Distance measurement sensor | Measure distance | ST VL5310X | 15+ | 4€ | 60€
Temperature sensor | Measure temperature | LM75AIMM | 1 | 2€ | 2€
Rotation encoder | Count rotations | ENX10 EASY 128IMP (?) | 1 | 100€ | 100€
Total: |  |  |  |  | 173€
Prices taken from Digikey and rounded up!

## Slide 8: Actors
Actor | Task | Desired part | Units | Price per unit | Total
Motor driver | Motor driver | TI DRV8871DDAR | 1 | 2€ | 2€
HV generator | ? | ? | 1 | 200€ (?) | 200€
Total: |  |  |  |  | 220€

## Slide 9: Interface to OBC
Roach(1): USB UART
  According to Paul: Problems with UART and Pi fixed
But: better solution desired
This may be: Ethernet
  Flexibel cable (industrial cables etc.) => Structure&thermal + electronics input awaited
  High performance: 100MBit/s
  If only a „simple“ FPGA is used, two options:
    Connect to FPGA internal Microblaze (requires IP license, test duration: 120days)
    Or: AXI Ethernet Lite MAC
      IEEE Std. 802.3 Media Independent Interface
      100MBit/s
  In case of a SoC: Ethernet directly to ARM core (maybe the best idea)

## Slide 10: Processor options
Which processor to choose? 

## Slide 11: Processor options
Idea from Cedric/Felix:
  Pi Zero (approx. 6x3cm)
Idea from Matthias:
  FPGA industrial processing board (approx 4x3cm or 4x5cm)
Request to Xilinx regarding Xilinx University Program (XUP)
  Recommendation from Cathal (XUP): Zynq or Zynq Ultrascale SoC
  Zynq Ultrascale is too expensive and too powerful (large FPGA + quad core ARM + dual core realtime ARM + GPU in one SoC, depending on modul)
  Zynq maybe an interesting idea

## Slide 12: Processor options
Category | Pi Zero | FPGA (Artix-7 35T or 100T) | Zynq SoC (Z-7020)
Processor | 1GHz single core | - (softcore Microblaze up to 200MHz) | 667MHz dual core
Programmable logic | - | 35T: 33280 logic cells, 90 DSP, 1,8MBit BRAM, 250 I/O pins max 100T: 101440 logic cells, 240 DSP, 4,860MBit BRAM, 300 I/O pins max | 85000 logic cells, 220 DSP, 4,9MBit BRAM, 200+128 I/O pins max
Board | Pi Zero | TE0710-02-35-2CF or TE0710-02-100-2CF | TE0724-02-20-1I
RAM | 512MB DDR2 | 512MB DDR3 | 1GB DDR3
Ethernet? | NO | YES (100MBit dual) | YES (1GBit single)
Costs | 6€ | 142€ / 214€ | 240€

## Slide 13: Processor options
Pi Zero has NO Ethernet
  External board required (via GPIO or USB)
  No way to reach 1GBit
  Additional hardware efforts (USB solution not feasible for integration in rover)
Artix-7 FPGA
  Powerful and energy efficient solution (energy consumption depends heavily on frequency, FPGA operates in lower frequency as normal processor and is still faster through parallelization)
  Microblaze microprocessor: programmed in C/C++
  Hardware: VHDL, Verilog

## Slide 14: Processor options
Xilinx XUP suggestions: Zynq
  System on Chip (SoC) solution
  Dual core ARM + FPGA fabric
  1GBit Ethernet to ARM core
  Interesting option (maybe Pi experience can be reused)
  But: higher power consumption than normal FPGA
Conclusion:
  Pi Zero has no direct ethernet support (only using additional module and with lower speed expected in case of GPIO)
  Small FPGA already fulfils all requirements
  Zynq processor might be interesting for KSat as dual core ARM is integrated (programming with C/C++, even a Python option is available)
    Linux or FreeRTOS possible => keep it as simple as possible => NO Linux, better REAL realtime operation system

## Slide 15: Processor options
Costs for FPGA or FPGA SoC option:
  Expecting: two FPGA boards and one carrier board
  Optional: one or two evalboards (depending on XUP output)
Option FPGA (Artix-7 35T):
  2x 142€ + 180€
  1x 72€
  Gesamt: 536€ (Kosten FPGA Boards + Entwicklungsequipment)
Option FPGA (Artix-7 100T):
  2x 214€ + 180€
  1x 270€
  Gesamt: 878€ (Kosten FPGA Boards + Entwicklungsequipment)
Option FPGA SoC (Zynq):
  2x 240€ + 200€*
  1x 200€
  Gesamt: 880€ (Kosten FPGA SoC Board + Entwicklungsequipment)

## Slide 16: Processor options
Costs for FPGA or FPGA SoC option:
  Expecting: two FPGA boards and one carrier board
  Optional: one or two evalboards (depending on XUP output)
Option FPGA (Artix-7 35T):
  2x 142€ + 180€
  1x 72€
  Gesamt: 536€ (Kosten FPGA Boards + Entwicklungsequipment)
Option FPGA (Artix-7 100T):
  2x 214€ + 180€
  1x 270€
  Gesamt: 878€ (Kosten FPGA Boards + Entwicklungsequipment)
Option FPGA SoC (Zynq):
  2x 240€ + 200€*
  1x 200€
  Gesamt: 880€ (Kosten FPGA SoC Board + Entwicklungsequipment)
JTAG Adapter:
  Original Xilinx: ~300€
  Digilent adapter (fully compatible to Xilinx software and devices): ~50€
Before decision in next month: Try to order evaluation boards through XUP (which can take a few weeks)! Only possible after positive DLR decision!

## Slide 17: Processor options
Existing equipment:
  1x BASYS3
  1x NEXSYS VIDEO
  Both boards have Digilent JTAG on board (no Xilinx JTAG) and can be correctly detected, programmed and debugged from Vivado (so this would save us about 250€ on JTAG adapter costs)
Xilinx Vivado Design Suite is free of charge available at xilinx.com
  No need for ModelSim (single license can cost a multiply of the whole Roach2 budget)
  A limited ModelSim version for students is avaible
    Limited to 10.000 lines of code (if we use a lot of IP cores or have HLS output, this limited maybe reached)
  Xilinx Simulator is powerful enough and fully integrated in Vivado

## Slide 18: Processor options
Xilinx Vivado

## Slide 19: Xilinx XUP
Donation of boards possible, request has to be send from an IRS professor
Optional: Xilinx has it‘s own contest: OpenHardware 2019
  Only open for students (so I can only be listed as advisor)
  Should be possible to submit RCU
In case we get NO XUP donation, student prices:
  Zynq Zybo Z7-20: ~200€
    Camera interface (CSI)
    1GB DDR3 RAM
    Ethernet
  Nexys Video (Artix-7 200T): ~270€
    1GBit Ethernet
    512MB DDR3 RAM
    Large FMC connector
  Basys 3 (Artix-7 35T): ~72€
    No Ethernet (additional board required)
    No RAM

## Slide 20: System design
FPGA/SoC
Left side
Right side
Rear
Front
Top
Bottom
Distance measurement sensor
Ethernet
DDR3 RAM
SD Card
Rotation encoder
HV generator
Motor driver
IMU
Temperature sensor
Camera

## Slide 21: System design
Sensor | Number of data fields | Size per data field (bit) | Total (bit) | Update rate (Hz) | Number of sensors | Expected data rate (Bit/s)
Laser distance sensor | 1 | 16 | 16 | 50 | 18 | 14400
IMU | 9 | 16 | 144 | 40 | 1 | 5760
Rotation encoder | 1 | 16 | 16 | 5000 | 1 | 80000
Temperature sensor | 1 | 16 | 16 | 2 | 1 | 32
ADC voltage control | 1 | 16 | 16 | 100 | 6 | 9600
Internal logging | 1 | 16 | 16 | 10 | 1 | 160
Total: |  |  |  |  |  | 109952
Optional: Camera modul
Assuming a standard 5MP camera: 1080p, RGB565 format, 30fps => 124,416MByte/s
As we only have a 100MBit Ethernet, we cannot send pictures at full step but every second e.g.
Assumed camera modul: https://reference.digilentinc.com/reference/add-ons/pcam-5c/reference-manual

## Slide 22: System design
Data should be streamed to OBC with a full data rate of Ethernet (max. 100MBit/s)
Data rate without images is about 100KBit/s => no problem so far
  Might be possible to use TCP instead of UDP without problems of package resend
Camera: only a small number of cameras can be used
  In case of Pi: we need full driver support
  In case of FPGA/SoC:
    Digilent has a cheap solution with a 5MP camera (see link on previous page)
    Required FPGA design and drivers are included (already complete for Zynq, Artix-7 would require more work)
  See: https://github.com/Digilent/vivado-library/blob/feature/d-phy/ip/MIPI_CSI_2_RX/docs/mipi_csi_2_rx.pdf
Final decision for camera should wait until first RCU is implemented!

## Slide 23: System design
OBC to RCU: Start
RCU: Self test
RCU (timer): Start experiment
RCU (timer): End experiment
End of power: End data acquisition

## Slide 24: Thank you for attention!
Please feel free to ask questions?